## Slide 1: TRIBHUVAN UNIVERSITY INSITUTE OF ENGINEERING, CENTRAL CAMPUS DEPARTMENT OF MECHANICAL ENGINNERING PULCHOWK, LALITPUR INSTUMENTATION AND FLOW VISULIZATION OF OPEN CIRCUIT WIND TUNNEL AT DEPARTMENT OF MECHANICAL ENGINEERING PRESENTED BY YUBRAJ KAWAR (072/BME/647) YUGAL KRISHNA SHRESTHA (072/BME/648) SAMAN DHAKAL (072/BME/651) PRESENTATION ON PROPOSAL DECEMBER 2018

## Slide 2: Outline of the Presentation
Introduction
Rationale of project
Problem Statement
Project Purpose
Conceptual Framework and Methodology
Expected Outcomes
Schedule
References

## Slide 3: INTRODUCTION
Wind tunnels are used to test models and to measure the force exerted by the fluid in the model and the obtained result can be used to predict on the full-scale model. Wind tunnels are designed for specific purpose and speed range.
The wind tunnel present in the Department of Mechanical Engineering’s lab is of open loop type. Contraction section consists coarse screen at the inlet followed by honeycomb and anti-turbulence screens to decrease the turbulence of air. Diffuser section consists of centrifugal fans at outlet to suck the air from inlet. There are 16 motors with centrifugal blades which produces the air velocity of 12 m/s. Pitot probe is used in velocity measurement and manometer in pressure measurement.
Usage of the wind tunnel dates back to several years. But due to lack of maintenance, the tunnel is currently out of order.

## Slide 4
Wind Tunnel At our Department:
Contraction Section:
1200mm*1200mm
Honey-comb and anti-turbulence screens
Test Section:
250mm*250mm
Transparent
Diffuser section:
650mm*650mm
16 centrifugal motors (1400 watt, 500 watt)
Air velocity 12m/s
Pitot tube and manometer

## Slide 5: Flow Simulation
Defination
Show laminar, turbulent, vortex, boundary layer separation.
Surface Flow Visualization
fluorescent dye, oil or special clay mixtures
Turfs: Small filaments soaked in UV dye, better view in UV light, glued in model
China clay: Mixture of kerosene, clay powder and DayGloTM pigment
Wind StartVapourize kerosene leaving flow pattern
Long lasting, cannot change model during flow visualization
Sublimation naphalene and trichlorothaneleaves flow pattern at turbulent region

## Slide 6
Off the surface visualization.
Tracers such as smoke particles, hydrogen and helium soap bubbles, aniline and methylene dye, aluminium powder and polystyrene particles.
Smoke Flow Visualization:
Smoke generator and probe to insert smoke
Mineral oil( Kerosene, paraffin), buring wood, paper or tobacco or vapourize substance containing bromide or chloride, laser lighter better

## Slide 7
Optical Methods:
Visualize compressible flows
Angular deflection, vertical displacement, phase shift
Shadow, schlieren and interferometry
Special Methods:
Heat energy adding, refractometry, laser light sheet, particle velocimetry
E.g. Heat energy addingdensity variationOptical techniques for visualization
E.g. Shooting of electronexcitationrelease lightVisualizes flow patterns.

## Slide 8: NEED AND IMPORTANCE OF PROJECT
This project is stressed to be completed as soon as possible due to absence of any other functional wind tunnel available in the department or the campus, which is a very basic apparatus in the sector of aerodynamics.
Current period is also a suitable timing for this project as it would help to enhance the lab of aerospace engineering which is a recently added program in the campus.
Through this project, the present and future generations of students of the mechanical engineering and aerospace engineering would get enormous facilities to use tunnel for various testings.

## Slide 9: RATIONALE
Familiarizing to the wind tunnel mechanism
Design and simulation for proper instrumentation
Fulfilling requirements of the wind tunnel in the department
Testings of the tunnel

## Slide 10: PROBLEM STATEMENT
Currently the tunnel testing apparatus is out of order for few years now, hence Selection of high cost instrumentation has to be done for low cost wind tunnel.
Proper study of the pumps has not been done so air suction system reliability is unknown
Absence of proper mechanism for visualization and instrumentation in the wind tunnel.

## Slide 11: PROJECT OBJECTIVES
Main objective
To characterize instrument and implement flow visualization technique for the low subsonic open-circuit wind tunnel at department of ME.
Specific objectives
To determine the parameters for tunnel characterization.
Installation of tunnel mountings.
To determine and install suitable apparatus for flow visualization.

## Slide 12: CONCEPTUAL FRAMEWORK AND METHODOLOGY
Literature review
Accessories Selection and maintenance of Wind tunnel
Design and simulation of instrumentation
Fabrication of test model
Tunnel testing and comparison with CFD results

## Slide 13: EXPECTED OUTCOME
Development of mounting apparatus for model mounting (vertical, horizontal, lateral), load cell, torsion bar, tachometer, etc.
Characterization by flow simulation and its validation will be checked using tunnel experiment.
Obtaining laminarization by adjustment of tunnel geometry in case if the flow in tunnel core section is perturbed/disturbed.
Flow visualization using compressed gas that does not mix with the core flow will be tested.

## Slide 14: TIME SCHEDULE
Chart: Gantt Chart
| Tunnel Characterization | Mounting and instrumentation System | Flow visualization | Post Processing and reporting
Start Date | 43463 | 43553 | 43614 | 43675
Days for Completion | 90 | 60 | 60 | 30

## Slide 15: REFERENCES
https://www.grc.nasa.gov/www/k-12/WindTunnel/history.html
https://www.grc.nasa.gov/www/k-12/airplane/tuntype.html
https://flight.engr.ucdavis.edu/facilities/aeronautical-wind-tunnel/
http://mech.pcampus.edu.np/index.php/faculty-and-research/dme-reseach-facilities/subsonic-wind-tunnel-facility-ioe-nepal/
http://vlab.amrita.edu/?sub=77&brch=297&sim=1671&cnt=3605
https://users.cg.tuwien.ac.at/helwig/diss/node10.htm
https://www.aa.washington.edu/AERL/KWT/techguide/flowviz
https://www.onera.fr/en/windtunnel/model-support
https://www.grc.nasa.gov/www/k-12/airplane/tunbalmnt.html