## Slide 1: Pelton Turbine

## Slide 2: HYDRAULIC TURBINES
Introduction:
The device which converts hydraulic energy into mechanical energy or
vice versa is known as Hydraulic Machines. The hydraulic machines
which convert hydraulic energy into mechanical energy are known as
Turbines and that convert mechanical energy into hydraulic energy is
known as Pumps.
Fig. shows a general layout of a hydroelectric plant.

## Slide 4: Turbines:
Impulse
  Pelton wheel
  Turgo
  Crossflow
Reaction
  Radial (e.g. Francis)
  Axial (e.g. propeller, bulb, Kaplan)

## Slide 5: layout of a hydroelectric plant
1. A Dam constructed across a river or a channel to store water. The reservoir is also known as Headrace.
2. Pipes of large diameter called Penstocks which carry water under pressure from storage reservoir to the turbines. These pipes are usually made of steel or reinforced concrete.
3. Turbines having different types of vanes or buckets or blades mounted on a wheel called runner.
4. Tailrace which is a channel carrying water away from the turbine after the water has worked on the turbines. The water surface in the tailrace is also referred to as tailrace.

## Slide 7
Contains:
  Introduction
  construction
  Working
  Calculation ( v )
  Design aspects
  
  Pelton turbine in Nepal
  Problems

## Slide 8
1.Introduction :
    It is impulse turbine.
    Pressure energy is converted into KE when passed through nozzle.
    Free high velocity water jet impinge on the bucket mounted on the periphery of the runner.
    Impulse force on the bucket rotates the runner.

## Slide 10
Construction (different Parts):
    Max. 6 nozzles

## Slide 12: Pelton Turbine

## Slide 15
Bucket:

## Slide 16
Nozzle striking the bucket:

## Slide 22: Spear valve and jet deflector

## Slide 23: When to use a Pelton turbine

## Slide 24
3.Working-1:
    All the PE is converted into KE at nozzle.
    Pressure all over the wheel is Patm.
    Energy transfer is purely impulse action.

## Slide 25
3.Working-2:
    Governing mechanism: To keep runner speed constant by varying flow rate when load fluctuate.
    Inlet angle at the jet is 1~3 due manufacture difficulty.
    Deflection angle is 165~170  not to disturb incoming jet.

## Slide 26
Combine spear and deflector operation to control turbine:

## Slide 33
4.Calculations Velocity -1:
N= speed of wheel in rpm
D= diameter of the wheel
d= diameter of jet
u= peripheral (circumferential) velocity of runner
= it will be same at inlet and out let of the runner at mean pitch. ( ie u=u1=u2)
= (DN) / 60

## Slide 34
Calculations Velocity :Work done SKIP
Vl = absolute velocity of water at inlet, Vr1 =jet velocity relative to vane/bucket at inlet , = angle between the direction of the jet and direction of motion of the vane bucket (also called guide angle), = angle make by the relative velocity (Vr1 ) with the direction of motion at inlet (also called vane angle at inlet),

## Slide 35
Calculations Velocity :Work done SKIP
Vwl and Vf1 =the components of the velocity of the jet V1, in direction of motion and perpendicular to the direction of motion of the vane respectively, Vw1 is also known as velocity of whirl at inlet, Vf1 is also known as velocity of flow at inlet

## Slide 36
Calculations Velocity :Work done
V1,V12 , =0, =0, Vw1 ,Vf1 are corresponding values at inlet. V2,Vr2 , , , Vw2 ,Vf2 are corresponding values at outlet. Inlet. The velocity triangle at inlet will be a straight line where

## Slide 37
Calculations Velocity :Work done
Depending upon magnitude of the peripheral speed (u), the unit may have a slow, medium or fast runner and the angle R and Vwz will vary as follows: (i) Slow runner < 90° (Vw2 is -ve) (ii) Medium runner  = 90° (Vw2 = 0) (iii) Fast runner  > 90° (Vw2 is +ve) The force exerted by the jet of water in the direction of motion is given as

## Slide 38
Calculations Velocity :Work done
Vr1 = V1-u1=Vw1-u1 and Vr2 cos = Vw2+u2 Vw2= Vr2 cos -u2= Vr1 cos -u2=(V1-u1)cos -u2 u1=u2=u Now work done by tie jet on runner per second = F × u = aV1 (Vr1 + Vr2 cos ) ×u =aV1 (Vw1-u1 + Vw2+u2 ) ×u =aV1(Vw1+ Vw2)×u=aV1[V1+(V1-u1)cos-u2] ×u = aV1(V1-u1)(1+cos)×u H= work done per sec / KE of jet per sec = aV1(V1-u1)(1+cos)×u / 1/2×(aV1) V12 For Hmax d Hmax /du=0 then Hmax = (1+cos  ) / 2

## Slide 39: 5.Design aspects of pelton wheel-1:
Velocity of jet: The velocity of jet at inlet is given by:
V1 = Cv(2g H)
Cv = co-efficient of velocity (= 0•98 or 0.99)
H = net head on turbine.

## Slide 40: 5.Design aspects of pelton wheel-2:
2. Velocity of wheel: The velocity of wheel (u) is given by:
u = Ku2g H
Ku = speed ratio. It varies from 0.43 to 0.48

## Slide 41: 5.Design aspects of pelton wheel-3:
3. Angle of deflection of the jet: The angle of deflection of the jet through the buckets
is taken as 165° if no angle of deflection is given.

## Slide 42: 5.Design aspects of pelton wheel-4:
5. Mean diameter of the wheel (D): The mean diameter or the pitch diameter D of the Pelton wheel is given by
u= = (DN) / 60
D= 60u / N

## Slide 43: 5.Design aspects of pelton wheel-5:
5.Jet ratio (m): It is defined as the ratio of the pitch diameter (D) of the Pelton wheel to the diameter of the jet (d). It is denoted by `m' and is given as
m=D/d
m=lies between 1 1 and 16 for maximum hydraulic efficiency
Normally, the jet ratio is adopted as 12 in practice.

## Slide 44: 5.Design aspects of pelton wheel-6:
6.Bucket dimensions: Some of the main dimensions of the bucket of a Pelton wheel are as follows :
B= 3 to 4d; L=2 to 3d; T=0-8 to 1•2d ;
T
B
L

## Slide 45: 5.Design aspects of pelton wheel-7: Bucket dimensions:

## Slide 46: 5.Design aspects of pelton wheel-8 No. of nozzles:
Normally 1 nozzle or jet.
To produce more power with same wheel = no. of nozzles.
Max nozzles = 6
Normally not more than 2 nozzles for per vertical runner.
Normally not more than 4 nozzles for horizontal runner.
No. of nozzle = total Q through T/ Q through one nozzle

## Slide 47: 5.Design aspects of pelton wheel-8: No. of buckets (Z):
It should be such that the jet is always completely intercepted by the buckets so that vol is very close to 1.
        Z = 15 +D/2d

## Slide 48: 6. Hydraulic 1
H= power developed by the runner / power supplied at the inlet of T
= [aV1 (Vw1 + Vw2) ×u] / gHQa
= 90~95

## Slide 49: 6. Mechanical 2
M= power available at T shaft / power developed by the T runner
= shaft power / bucket power (power develop by runner)
= P / [aV1 (Vw1 + Vw2) ×u]
= 97~99
It is due to bearing friction etc.

## Slide 50: 6. Volumetric 3
V= [vol. of water actually striking the runner] / [total water supplied by the jet to the turbine]
= Qa /Q
= 97~99

## Slide 51: 6. Over all 4
O= [power available at the turbine shaft] / [power available from the water jet]
= shaft power / water power
= P / gHQ
= 85~90
O= H M V

## Slide 52: 6. generator( G ) 5:
6.Hydraulic electric plant efficiency-6:
HE = G O
HE = Pout of HE / gHQ
END OF PELTON TURBINE

## Slide 53: 7.Pelton turbine in Nepal
The major power plant having pelton turbine are
  Kulekhani first (30x2)MW
  Puwa khola (3x2) MW
  Sundarijal (300x2)KW
  Pharping (250x2)KW
  Khimti (12x5)MW
  Chilime (11X2)MW
  Adhikhola (1.7x3)MW
  Piluwa-turgo (1.5x2)MW